## Slide 1
Digital Design and Synthesis
COEN 6501

## Slide 2
Lecture_1
In this lecture we will review:
The Digital Design process
Introduce and review Adders
The Carry Ripple Through Adder
The Carry Look Ahead Adder

## Slide 3: System Design Description
Systems are described in terms of three domains:
Behavioural domain
Structural domain
Physical domain

## Slide 4
Structural
Behavioural
Physical
Logic Synthesis
Physical
Synthesis

## Slide 5
Structural
Behavioural
Physical
System
Algorithmic
Micro architecture
Logic
Circuit
Rectangles
Cells
Macro-cells
Modules
Chips, boards…
Processor
Hardware modules
ALU, registers
Gates, F/Fs
Transistors
Systems
Algorithms
Register transfer
Logic Equations
Transfer function
Logic synthesis
Physical
synthesis

## Slide 6
Expected power savings in logic synthesis at various levels of design flow
Level
Transformation
Expected Power Saving
Algorithmic
Algorithm selection
Orders of magnitude
Behavioural
Concurrency
Several times
Register Transfer Level
Structural transformations
~10 - 15%
Clock control
~10 - 90%
Data/signal encoding
~20%
Technology independent
Extraction/decomposition
~15%
Technology dependant
Technology mapping
~20%
Gate sizing
~20%
Layout
Placement
20%
Optimization Levels

## Slide 7
Design Process:
It starts with behavioural
description, decomposing
the high level of constructs
into more precise functional
units, then mapping these
units into physical elements.
System Specification
Architectural Design
(behavioural)
Analysis
Design Implementation
(structural)
Analysis
Design Implementation
(Physical)
Analysis

## Slide 8: Design Strategies
Hierarchy
  A repeated process of dividing large modules into smaller sub-modules until the complexity of sub-modules are at an appropriately comprehensible level of detail.
  Parallel hierarchy is implemented in all domains.

## Slide 9: A Structured Design
Regularity
  Divide the hierarchy in to similar building blocks whenever possible.
  Some programmability could be added to achieve regularity.
Modularity
  Well defined behavioural, structural and physical interface.
  Helps: divide tasks into well defined modules, design integration, aids in team design.
Locality
  Internals of the modules are unimportant to any exterior interface.

## Slide 10
System Design Methodology
Market Analysis
System Specifications
System Architecture
System Partitioning
Market windows
System features & requirements
Standards
Functional
Electrical
Mechanical
Environmental
Strategies
Modelling
Verification
Dictated by complexity, I/O pins, off-the-
shelf components, special requirements
Partitioning guidelines
Partitioning approaches: vertical,
horizontal, functional, performance

## Slide 11
Testability
Technology Selection
Detailed Design
Implementation
Strategies, chip testing, board
testing
Testability features
Penalties
Dictated by: speed, power
dissipation, driving capability,
cost, lead time
Logic design/synthesis
Optimization
Verification
Off-the-shelf ICs
Application Specific ICs

## Slide 12
Assembly
Testing
Documentation
Production
Decide on packaging technical components
Design/manufacture
Components
Electrical/mechanical assembly
Mechanical assembly & components sales
Functional
DC test
AC test
Burn-in
Technical documents
H/W & S/W & mechanical
User manual
Test document

## Slide 13
Verify at every step
Layout
Device
Circuit
Logic
Structural
CPU
MEMORY
Functional

## Slide 14: IC Design Methodology
Requirement specification
  most important function which impacts the ultimate success of an IC relates to how firm and clear the device specifications are.
  Device specification may be updated throughout the design cycle.
  Main items in the specifications are:
    functional intent: brief description of the device, the technology and the task it performs.
    Packaging specification
      device port number
      package type, dimension, material

## Slide 15: Functional Description
  Functional description
    high-level block diagram: all major blocks including intra block connections and connections to pin-outs indicating direction and signal flow.
    Intra block signal function: description of how blocks interact with each other supported with timing diagram where necessary.
    Internal block description of internal operation of each block. Where necessary, the following to be included: timing diagram, state diagram, truth table.

## Slide 16: Specifications
  I/O specifications
    pin-out diagram
    I/O functional description
    loading
    ESD requirements
    latch-up protection
  D.C. specifications
    absolute maximum ratings for: supply voltage, pin voltages
    main parameters: VIL and VIH for each input, VOL and VOH for each output, input loading, output drive, leakage current for tri-state operation, quiescent current, power-down current (if applicable)

## Slide 17: Specification, continued
  AC specifications
    inputs: set-up and hold times, rise and fall times
    outputs: propagation delays, rise and fall times, relative timing
    critical thinking
  Environmental requirements
    operating temperature, storage temperature, humidity condition (if applicable)
  Testing

## Slide 18: Device Specification
Functional intent: briefly describe the device, the technology, and the circuits it will replace as well as the task it will perform.
Design concept
    pin-out diagram: describe the device using a block diagram of the external view of the chip - basically, a box with all the I/O pins labelled and numbered
    I/O description: use a chart to define the I/O signals shown in the pin-out diagram

## Slide 19: Example:

## Slide 20: Functional Specification
    internal block diagram: draw blocks for major functions, show all connections including: connection to all pin-outs, connections between blocks, and direction of signal flow
    Inter-block signal function: describe how the blocks interact with each other and support this with timing diagrams where necessary
    internal block description: describe the internal operation of each block. When necessary, include: timing diagrams, state diagrams, and truth table
  Logic description: circuit schematic or logic
diagram using standard cell library components
Package description: device port number, package
type, dimensions, materials

## Slide 21: Operating characteristics Absolute maximum stress ratings. Example:

## Slide 22: Requirements
  Operating power and environmental requirement:
    power supply voltage
    operating supply current (specify conditions, e.g., power up, power down, frequency, output conditions)
    storage temperature
    operating temperature
    humidity conditions (if applicable)

## Slide 23: Input characteristics. Example chart: (V reference is VSS = 0, temperature range is 0oC to 70oC)

## Slide 24: Output Interface Characteristics Example chart: (VSS = 0, T range 0oC to 70oC

## Slide 25: AC description Timing diagram: include well-labelled signal drawings of all significant input and output relationships, rise and fall times, data set-up and hold times. Indicate the voltage range over which timing must be guaranteed
Definitions:
Cout
input
output
VIH
VIL
Set-up
hold
hold
VIH
VIL

## Slide 26: Example: timing diagram and chart
RXCK
RXFRM
RXIN
t19
t20
t22
t21
t17
t18
t16

## Slide 27: Specs (continued)

## Slide 28: Critical Path
Signal paths with ‘tight’ timings (if applicable)
potential ‘race’ conditions (if applicable)
any set of paths with the same source and destination such as a clock signal and its complement (if applicable)

## Slide 29: Test Description
Test strategy: written description of functions to be tested. This section is a guide for determining and explaining simulation patterns
simulation input/output patterns: timing diagrams which include stimulus to be applied to input pins and the expected response on the output pins

## Slide 30
Example :
Multiplicand = 100010012 = 8916
Multiplier = 101010112 = AB16
Expected Result = 1011011100000112 =5B8316

## Slide 31: System Level Design
Top down approach
Using behavioural constructs, top level architecture is defined
Design validation is technology independent
Use HDL to model the design (e.g., VHDL and Verilog)
RTL is efficient for describing data flow

## Slide 32: System Level design (Continued)
Timing verification is difficult unless structure logic is defined
VHDL representation can be changed into structural logic through - manual design, design synthesis: automated process which involves the conversion of VHDL/RTL into a set of registers and combinational circuits

## Slide 33
Synthesis report

## Slide 34
Area report after Synthesis

## Slide 35
Power report after Synthesis

## Slide 36
Timing Report After Synthesis

## Slide 37: AIMs
What the CUSTOMER wants
High Quality
Low Cost
Small Size/Weight
What the EMPLYER wants
Design the:
Best
Cheapest
In shortest time
Follow the Spec or better.
What you CHIP DESIGNER should do:
Design a chip with:
High speed
Small area
Low power
Testable and reliable
Delivered in a short time

## Slide 38: Logic Design
Evaluation of library constructs (basic & macro) function, timing, area
Logic minimization
NAND/NOR transformation
Buffering
Fan-out reduction
Fan-in reduction

## Slide 39: Logic Level design (Continued)
Critical timing
Priority routing
I/O compatibility
Logic optimization
Cost function: area, speed, power, or a combination

## Slide 40: Logic Simulation
Simulation is the process of exercising a theoretical model of the design as a function of time for some applied input sequence
Logic simulation is to aid in verification of a digital system

## Slide 41: Logic Simulation (Continued)
Components
  models: functional, timing
  connectivity: a description of how the basic components are connected together
  stimulus: 1’s and 0’s that are applied at specific times to the primary inputs of the design
  simulation control
States: basic (0, 1, X), strength could be combined with basic; strong (S), resistive (R), high impedance (Z), indeterminate (I)

## Slide 42
Simulation model
- logical
***************************************************
** Library: ACME
** Technology: 2u CMOS
** Part: fdrc
**
** Description: D flip-flop with rising edge, async. Clear
***************************************************
model fdrc: table
input d, rn;
edge_sense input cp;
output q, qn;

## Slide 43
State_table
rn, cp, d, q :: q, qn;
***** ------------------------------------------------------------
0, (??), ?, ? :: 0, 1,
1, (01), ?, ? :: (d), !(d);
1, (?0), ?, ? :: N, !(q);
1, (1?), ?, ? :: N, !(q);
end (fdrc: table);

## Slide 44: Timing Verification
Process of making accurate delay prediction and to detect timing violation in the design. These violations include set-up time, hold time, races and spikes.
Delay through the circuit is a function of:
  intrinsic delay
  number of loads connected to each net
  temperature
  voltage
  process variation, layout
Typically, best and worst case scenarios should be considered.

## Slide 45: Simulator uses a set of equations to calculate exact delays
Fan-out
  td = t(int) + K*L
  t(int) = intrinsic delay
  K = drive factor
  L = sum of equivalent loads

## Slide 46: Timing Verification (Continued)
temperature td = td/FT FT = (T2/T1) -M
voltage t’d = td/[VDDr(1 + 0.0f)]
process t’d = td(1 + 0.01Fp), Fp = = processing variation factor
layout information is normally supplied in two forms:
  pre-layout estimation
  post-layout: back annotation

## Slide 47: Timing
hazards
  spikes: inertial and transport delays
  set-up time/hold time/minimum pulse width
tPLH = 2
tPHL = 1
inertial
transport

## Slide 48: Timing
Critical path analysis
  detection of timing violation for data path structure
  the process is simply adding up path delays and compute the result with the period of the clock at the destination (F/F)
  path analysis is not simulation and does not utilize information about the functionality of the device
  look for two parameters
    hold slack = clock period - hold path time
    set up slack = clock period - set up path time
    slack >= 0
    paths are chosen to provide the least amount of available set up or hold times

## Slide 49: Structural layout synthesis
Floor planning
  it is the exercise of arranging blocks of layout within a chip to minimize area or to maximize speed
  floor plan editors provide graphical feedback about the size and placement of modules (without showing details), also the connectivity information between the modules in the form rat’s-not
  floor planning could be done manually, or automatically with manual intervention
  factors influencing floor planning (core & I/Os)

## Slide 50
A
B
C
D

## Slide 51: Placement and routing
Placement: is the task of placing modules adjacent to each other to minimize area or cycle time
two algorithms: min-cut, simulated annealing
routing: a router takes a module placement and a list of connections, connects the modules with wires
types of routers: channel, switch box, maze

## Slide 52
inv
inv
reg
nd2
nd2
nd2
nd2
nd2
nd2
nd2
nd2
inv
inv
inv
inv
inv
reg
nd3
nd3
nd3
Channel route
Channel route

## Slide 53: Layout
Other layout tools
  synthesis
  compaction
Layout verification
  design rule checking
  layout extraction
  layout vs. schematic
Back annotation of post layout simulation

## Slide 54: Testing
  to verify the correct operation of the device by exercising it by a set of test patterns, and then to check the output patterns to see whether they are identical to the ones predicted by the simulator
  tester also verifies DC and AC parameters on the pins of the device
comparator
DUT
X 0 1 1
0 1 0 1
Z 1 1 1
: : : :
0 1
1 0
0 1
: :
from
simulator
o/p
i/p

## Slide 55: Timing Analysis
  Tester operates in a periodic fashion
  input signals charge states at the beginning of the test period
  output signals are strobed at the end of the period to determine whether the measured values matches the simulated values..
T0
T0
T0
Test
cycle
i/p
o/p
strobe

## Slide 56: Types of Testing
Functional (mostly at lower speeds)
  static
  dynamic (refresh if required)
DC test
  continuity
  leakage, power consumption
  high/low voltage levels, drive capability
AC test
  rise/fall times, propagation delays
  set-up and hold times, access times

## Slide 57
Functional unit
Functional unit
Functional unit
Processor
register
register
register
LOGIC
CIRCUIT
LAYOUT
FABRICATION
COEN 7501
Formal Verification
ENCS 6521
Design for Testability
ELEC 6231
COEN 6531
ASIC Synthesis
ENCS 6511
ELEC 6241
ELEC 6501
COEN 7741
Advance Comp. Arch

## Slide 58: Binary Arithmetic

## Slide 61: Example: design an addition overflow circuit, in accordance with the following specification:
When the operation is addition and both addend and augend are +ve, overflow is indicated by a carry from the most significant digit (MSD)
when the operation is addition and both addend and augend are -ve, overflow is indicated by the absence of carry from the MSD
when the operation is subtraction and the minuend is +ve and the subtrahend -ve, overflow is indicated by a carry from the MSD
when the operation is subtraction and the minuend is -ve and subtrahend is +ve, overflow is indicated by absence of a carry from the MSD

## Slide 62
THE END